2D Scanner

User manual

(ver1.0)

directory

Operation guide………………………………………………………………………….................................4

Basic performance..……………………………………………………………….............................................5

Set up process.…………………………………………………………………….............................................5

Scan function

Output mode…………………………………………………………………………….................................6

Baud rate………………………………………………………………………….............................................6

Keyboard language…………………………………………………………………………….........................6

Keyboard key set……………………………………………………………………….....................................7

Case format conversion…………………………………………………………….....................................7

Buzzer……………………………………………………………………………....................................8

LED…………………………………………………………………………….................................8

Power saving mode…………………………………………………………………….................................8

Read code successfully settings…………………………………………………….................................8

Decoding mode……………………………………………………………………….................................9

Same barcode re-read settings…………………………………………………………….................................9

White light setup…………………………………………………………………………...............................10

Red light setup……………………………………………………………..................................................10

White bar code configuration……………………………………………………………..............................10

Suffix & Prefix……………………………………………………………………...............................10

Send delay………………………………………………………………………...............................11

Bar code parameter Settings

Bar code type can make/configuration is prohibited…………………………………….............................12

CODABAR…………………………………………………………………………………...........................12

Code 39………………………………………………………………………………...........................12

INTERVELAVED 25…………………………………………………………………………………………13

NEC 25…………………………………………………………………………………………………….13

Code 93……………………………………………………………………………………………………….13

Straight 25……………………………………………………………………………………........................13

MATRIX 25………………………………………………………………………………….........................14

CODE 11……………………………………………………………………………………….....................14

CODE 128…………………………………………………………………………………………………….14

GS1-128……………………………………………………………………………………………................14

TELEPEN……………………………………………………………………………………........................15

UPC-A…………………………………………………………………………………………......................15

UPC-E…………………………………………………………………………………………………..16

EAN-13…………………………………………………………………………………………………..17

EAN-8…………………………………………………………………………………………………18

MSI...............………………………………………………………………………………………………….19

GS1 DATABAR………………………………………………………………………………….............19

TRIOPTIC……………………………………………………………………………………….....................20

CODEBLOCK A……………………………………………………………………………….....................20

CODEBLOCK F……………………………………………………………………………….....................20

PDF 417………………………………………………………………………………….....................20

MICRO PDF417………………………………………………………………………………......................20

GS1 COMPOSITE……………………………………………………………………………………….21

QR CODE………………………………………………………………………………………………….21

MAXICODE………………………………………………………………………………………………….21

DATA MATIX CODE…………………………………………………………………………………….21

AZTEC CODE…………………………………………………………………………………………….22

HAN XIN CODE…………………………………………………………………………………………….22

CHINA POST……………………………………………………………………………………………….22

KOREA POST………………………………………………………………………………………….…...22

Appendix

Appendix 1：Data Code……………………………………………………………………………………..23

Appendix 2：The white after restore factory settings…………………………………………….…………..24

Appendix 3：Common problems……………………………………………………………………………..25

Appendix 4：Standard ASCII codes…………………………………………………………………………..26

Appendix 5：Barcode type list………………………………………………………………………………..27

Appendix 6：Wireless configuration(RF6800)………………………………………………………………..27

Operation guide

1. The barcode scanner before the focus area, when the laser is enabled, as shown in the left lower figure, laser and barcode is not completely into 90 °, scanning effect best, effective to + 65 ° inclined Angle, up and down or so effective Angle of plus or minus 60 °, rotation Angle for the plus or minus 42 ° effectively. When scanning the barcode, please let the laser to cover the entire bar code, otherwise will not be able to read the correct data, as shown in the upper；

2. The optimal scanner read distance of 2-8 cm, has nothing to do with the density of the bar code size；

3. An acousto-optic scanner decode after a successful prompt. If no bar code, will enter dormancy；

4. The scanner if decoding is not successful, could the code system is not compatible or other reasons, please contact the after sales.

Basic performance

◎ Does support serial RS232 interface and standard USB2.0 interface;

◎ Have set the bar code scanning for basic Settings;

◎ Does support keyboard output of more than 30 different countries;

◎ Does support bar code editor, including adding suffix before a character or string, character case conversion;

◎ It was not support the ASCII character set;

◎ To support more than 30 kinds of different types of code, including a dimensional barcode and two;

◎ Does the barcode resolution minimum 4 mil;

◎ Have two kinds of barcode is triggered, a handheld scanner, since the sensor scans;

◎ When scanning output using advanced decoding algorithms, scan decode validation for many times, to ensure the ultra low bit error rate;

◎ To support the white barcode scanning;

◎ The default serial port baud rate in the 115200 baud.

Set up process

Find the corresponding bar code can be set. For example, when the item set too much need to restore the factory Settings, please scan "restore the factory Settings"

Restore the factory Settings

Output mode

USB Mode                                       USB Apple Mode

RS232 Mode                                     USB COM

Baud rate

9600                                              19200

57600                                             115200

Keyboard language

Keyboard default Settings

USA						                          French

German					                          Italy

Keyboard key set

CAPS LOCK Disable	                             CAPS LOCK Enable

Shift Lock Disable					              Auto detect the

keyboard Caps Lock

Case format conversion

The keyboard case

no conversion

All lowercase		                                All uppercase

Buzzer

Buzzer Enable						                   Buzzer Disable

LED

LED Enable						                   LED Disable

Power saving mode

Timeout value set

Read code successfully settings

Delay configuration

No Delay						                500MS Delay

1000MS Delay					                     1500MS Delay

Decoding mode

Manual mode                                    Auto scanning mode

Same barcode re-read settings

Reread delay time                               500MS

configuration

1000MS						                     2000MS

White light setup

White Light Enable                                White Light Disable

Red light setup

RED Light Enable						            RED Light Disable

White bar code configuration

Read only the white bar code

Normal barcode and                         Read only normal

reverse adaptive                                   barcode

Suffix & Prefix

Suffix CR						                Suffix CR+LF

Suffix TAB

Add the prefix                                      Remove all prefix

Add the suffix                                      Remove all suffix

Send delay

Characters Transmission delay                    Bar code time delay

Bar code type can make/configuration is prohibited

All types of barcode Enable                All types of barcode Disable

CODABAR

CODABAR Enable                                 CODABAR Disable

Transmit the starting                               Don't start and

and end operator                                   stop sign

Code 39

Code 39 Enable                                    Code 39 Disable

Transmit the starting                               Don't start and

and end operator                                   stop sign

Full ASCII Sign Enable                         Full ASCII Sign Disable

INTERVELAVED 25

INTERVELAVED 25 Enable                  INTERVELAVED 25 Disable

NEC 25

NEC 25 Enable                                    NEC 25 Disable

Code 93

Code 93 Enable                                   Code 93 Disable

Straight 25

Straight 25 Enable                                 Straight 25 Disable

Straight 25 IATA Enable                        Straight 25 IATA Disable

MATRIX 25

MATRIX 25 Enable                                 MATRIX 25 Disable

CODE 11

CODE 11 Enable                                   CODE 11 Disable

CODE 128

CODE 128 Enable                                  CODE 128 Disable

GS1-128

GS1-128 Enable                                   GS1-128 Disable

TELEPEN

TELEPEN Enable                                  TELEPEN Disable

UPC-A

UPC-A Enable                                     UPC-A Disable

Send check digit                               Don't send check digit

To transmit digital                                        Don't transmit digital

system characters                                        system characters

According to the two                              Hide the two

additional code                                    additional code

According to the five                              Hide the five

additional code                                    additional code

UPC-E

UPC-E Enable                                     UPC-E Disable

Open extension                                   Close the extension

12 UPC - A format                                 12 UPC - A format

Send check digit                               Don't send check digit

To transmit digital                                Don't transfer digital

system characters                                system characters

According to the two                              Hide the two

additional code                                    additional code

According to the five                              Hide the five

additional code                                    additional code

EAN-13

EAN-13 Enable                                    EAN-13 Disable

Send check digit                               Don't send check digit

According to the two                              Hide the two

additional code                                    additional code

According to the five                              Hide the five

additional code                                    additional code

ISBN symbols transmitted                     Don't send ISBN symbol

EAN-8

EAN-8 Enable                                     EAN-8 Disable

Send check digit                               Don't send check digit

According to the two                              Hide the two

additional code                                    additional code

According to the five                              Hide the five

additional code                                    additional code

MSI

MSI Enable                                        MSI Disable

GS1 DATABAR

GS1 DATABAR                                    GS1 DATABAR

OMNIDIRECTIONAL Enable                       OMNIDIRECTIONAL Disable

GS1 DATABAR                                    GS1 DATABAR

Limited Enable                                    Limited Disable

GS1 DATABAR                                    GS1 DATABAR

EXPANDED Enable                                EXPANDED Disable

TRIOPTIC

TRIOPTIC Enable                                  TRIOPTIC Disable

CODEBLOCK A

CODEBLOCK A Enable                        CODEBLOCK A Disable

CODEBLOCK F

CODEBLOCK F Enable                         CODEBLOCK F Disable

PDF 417

PDF 417 Enable                                   PDF 417 Disable

MICRO PDF417

MICRO PDF417 Enable                         MICRO PDF417 Disable

GS1 COMPOSITE

GS1 COMPOSITE Enable                     GS1 COMPOSITE Disable

GS1change UPC/EAN Enable            GS1 change UPC/EAN Disable

QR CODE

QR CODE Enable                                  QR CODE Disable

MAXICODE

MAXICODE Enable                                MAXICODE Disable

DATA MATIX CODE

DATA MATIX CODE Enable                  DATA MATIX CODE Disable

AZTEC CODE

AZTEC CODE Enable                            AZTEC CODE Disable

HAN XIN CODE

HAN XIN CODE Enable                         HAN XIN CODE Disable

CHINA POST

CHINA POST Enable                             CHINA POST Disable

KOREA POST

KOREA POST Enable                            KOREA POST Disable

Appendix 1: Data Code

0                                             1

2                                             3

4                                             5

6                                             7

8                                             9

A                                             B

C                                             D

E                                             F

Save                                      Discarded

Appendix 2: The white after restore factory Settings

Restore the factory Settings

Appendix 3: Common problems

The problem 1: read the bar code, bar code data will be lost?

Solution: slow down the transmission speed of the bar code reader.

The problem 2: barcode character garbled words and wrong?

Solution: set a bar code reader keyboard nations with using the keyboard.

The question 3: bar code can't read?

Solution 1: you read by the kinds of bar code decoder was shut down, suggest open item is set.

Solution 2: barcode encoding is not correct, contact technical support.

The question 4: when I connect the barcode gun to the PC serial port, can't get the boot prompt?

Solution: the PC serial port does not provide power supply, suggested that external + 5 v power or from the PC.

The question 5: when I'm going to a serial port barcode gun after receiving PC terminal, can get the boot prompt, but no data transfer?

Solution: output pins or communication protocol error. Examine the output pins or agreement, make it match the current use of PC terminal.

The question 6: decoding with voice prompt, but cannot be transmitted to the computer?

Solution: may be set to remove the decoder and you have the same barcode string, restore the same as the decoder input Settings.

The question 7: I can't find to set function of bar code?

Solution: because there are so many bar code need to be printed, and in this manual only some commonly used bar code printing. You can also set the content production according to print bar code you need.

Appendix 4:  Standard ASCII codes

| Dec | Hex | Abbreviations /character |  | Dec | Hex | Abbreviations /character |  | Dec | Hex | Abbreviations /character |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | NUL(null) |  | 43 | 2B | + |  | 86 | 56 | V |
| 1 | 1 | SOH(start of headling) |  | 44 | 2C | , |  | 87 | 57 | W |
| 2 | 2 | STX (start of text) |  | 45 | 2D | - |  | 88 | 58 | X |
| 3 | 3 | ETX (end of text) |  | 46 | 2E | . |  | 89 | 59 | Y |
| 4 | 4 | EOT (end of transmission) |  | 47 | 2F | / |  | 90 | 5A | Z |
| 5 | 5 | ENQ (enquiry) |  | 48 | 30 | 0 |  | 91 | 5B | [ |
| 6 | 6 | ACK (acknowledge) |  | 49 | 31 | 1 |  | 92 | 5C | \ |
| 7 | 7 | BEL (bell) |  | 50 | 32 | 2 |  | 93 | 5D | ] |
| 8 | 8 | BS (backspace) |  | 51 | 33 | 3 |  | 94 | 5E | ^ |
| 9 | 9 | HT (horizontal tab) |  | 52 | 34 | 4 |  | 95 | 5F | _ |
| 10 | 0A | LF (NL line feed, new line) |  | 53 | 35 | 5 |  | 96 | 60 | ` |
| 11 | 0B | VT (vertical tab) |  | 54 | 36 | 6 |  | 97 | 61 | a |
| 12 | 0C | FF (NP form feed, new page) |  | 55 | 37 | 7 |  | 98 | 62 | b |
| 13 | 0D | CR (carriage return) |  | 56 | 38 | 8 |  | 99 | 63 | c |
| 14 | 0E | SO (shift out) |  | 57 | 39 | 9 |  | 100 | 64 | d |
| 15 | 0F | SI (shift in) |  | 58 | 3A | : |  | 101 | 65 | e |
| 16 | 10 | DLE (data link escape) |  | 59 | 3B | ; |  | 102 | 66 | f |
| 17 | 11 | DC1 (device control 1) |  | 60 | 3C | < |  | 103 | 67 | g |
| 18 | 12 | DC2 (device control 2) |  | 61 | 3D | = |  | 104 | 68 | h |
| 19 | 13 | DC3 (device control 3) |  | 62 | 3E | > |  | 105 | 69 | i |
| 20 | 14 | DC4 (device control 4) |  | 63 | 3F | ? |  | 106 | 6A | j |
| 21 | 15 | NAK (negative acknowledge) |  | 64 | 40 | @ |  | 107 | 6B | k |
| 22 | 16 | SYN (synchronous idle) |  | 65 | 41 | A |  | 108 | 6C | l |
| 23 | 17 | ETB (end of trans. block) |  | 66 | 42 | B |  | 109 | 6D | m |
| 24 | 18 | CAN (cancel) |  | 67 | 43 | C |  | 110 | 6E | n |
| 25 | 19 | EM (end of medium) |  | 68 | 44 | D |  | 111 | 6F | o |
| 26 | 1A | SUB (substitute) |  | 69 | 45 | E |  | 112 | 70 | p |
| 27 | 1B | ESC (escape) |  | 70 | 46 | F |  | 113 | 71 | q |
| 28 | 1C | FS (file separator) |  | 71 | 47 | G |  | 114 | 72 | r |
| 29 | 1D | GS (group separator) |  | 72 | 48 | H |  | 115 | 73 | s |
| 30 | 1E | RS (record separator) |  | 73 | 49 | I |  | 116 | 74 | t |
| 31 | 1F | US (unit separator) |  | 74 | 4A | J |  | 117 | 75 | u |
| 32 | 20 | (space) |  | 75 | 4B | K |  | 118 | 76 | v |
| 33 | 21 | ! |  | 76 | 4C | L |  | 119 | 77 | w |
| 34 | 22 | " |  | 77 | 4D | M |  | 120 | 78 | x |
| 35 | 23 | # |  | 78 | 4E | N |  | 121 | 79 | y |
| 36 | 24 | $ |  | 79 | 4F | O |  | 122 | 7A | z |
| 37 | 25 | % |  | 80 | 50 | P |  | 123 | 7B | { |
| 38 | 26 | & |  | 81 | 51 | Q |  | 124 | 7C | ¦ |
| 39 | 27 | ' |  | 82 | 52 | R |  | 125 | 7D | } |
| 40 | 28 | ( |  | 83 | 53 | S |  | 126 | 7E | ~ |
| 41 | 29 | ) |  | 84 | 54 | T |  | 127 | 7F |  |
| 42 | 2A | * |  | 85 | 55 | U |  |  |  |  |

Appendix 6: Barcode type list

| Code Type | AIM ID | Possible AIM ID defined parameters | CODE ID | CODE ID Hexadecimal |
| --- | --- | --- | --- | --- |
| All Code |  |  |  | 99 |
| Code128 | ]Cm | 0,1,2,4 | j | 6A |
| GS1-128 | ]C1 |  |  | 49 |
| EAN-13 | ]E0 |  | d | 64 |
| EAN-13 with Add-On | ]E3 |  | d | 64 |
| EAN-13 with Extended Coupon Code | ]E3 |  | d | 64 |
| EAN-8 | ]E4 |  | D | 44 |
| EAN-8 with Add-On | ]E3 |  | D | 44 |
| Matrix 2 of 5 | ]X0 |  | m | 6D |
| Code49 | ]Tm | 0,1,2,4 | I | 6C |
| Code 32 | ]X0 |  |  | <3C |
| Code 39 | ]Am | 0,1,3,4,5,7 | b | 62 |
| Britsh Post | ]X0 |  | B | 42 |
| Canadian Post | ]X0 |  | C | 43 |
| China Post | ]X0 |  | Q | 51 |
| Han Xin | ]X0 |  | H | 48 |
| Codebar | ]Fm | 0-1 | a | 61 |
| Codablock A | ]O6 | 0,1,4,5,6 | V | 56 |
| Codablock F | ]Om | 0,1,4,5,6 | q | 71 |
| Code 11 | ]H3 |  | h | 68 |
| Code 93 and 93i | ]Gm | 0-9,A-Z,a-m | i | 69 |
| Data Matrix | ]dm | 0-6 | w | 77 |
| Australian Post | ]X0 |  | A | 41 |
| Aztec Code | ]zm | 0-9,A-C | z | 7A |
| GS1 Composite | ]em | 0-3 | y | 79 |
| GS1 DataBar | ]em | 0 | y | 79 |
| InfoMail | ]X0 |  | , | 2c |
| Intelligent Mail Barcode | ]X0 |  | M | 4D |
| Interleaved 2 of 5 | ]Im | 0,1,3 | e | 65 |
| Japanese Post | ]X0 |  |  | 4A |
| KIX (Netherlands)Post | ]X0 |  | K | 4B |
| Korea Post | ]X0 |  | ? | 3F |
| MaxiCode | ]Um | 0-3 | x | 7 8 |
| MicroPDF417 | ]Lm | 3-5 | R | 52 |
| MSI | ]Mm | 0 | g | 67 |
| NEC 2 of 5 | ]X0 |  | Y | 59 |
| OCR MICR (E 13 B) | ]o3 |  | O | 4F |
| OCR SEMI Font | ]o3 |  | O | 4F |
| OCR-A | ]o1 |  | O | 4F |
| OCR-B | ]o2 |  | O | 4F |
| PDF417 | ]Lm | 0-2 | r | 72 |
| Planet Code | ]X0 |  | L | 4C |
| Postal-4i | ]X0 |  | N | 4E |
| Postnet | ]X0 |  | P | 50 |
| QR Code and Micro QR Code | ]Qm | 0-6 | s | 73 |
| Straight 2 of 5 IATA | ]Rm | 0,1,3 | f | 66 |
| Straight 2 of 5 Industrial | ]S0 |  | f | 66 |
| TCIF Linked Code 39 (TLC39) | ]L2 |  | T | 54 |
| Telepen | ]Bm |  | t | 54 |
| UPC-A | ]E0 |  | c | 63 |
| UPC-A with Add-On | ]E3 |  | c | 63 |
| UPC-A with Extended Coupon Code | ]E3 |  | c | 63 |
| UPC-E | ]E0 |  | E | 45 |
| UPC-E with Add-On | ]E3 |  | E | 45 |
| UPC-E1 | ]X0 |  | E | 45 |

Appendix 6: Wireless configuration（RF6800）

Wireless search                  Wireless channel configuration

Rate of serial port

Factory default

Add suffix CR/LF                          Cancel suffix CR/LF

Add suffix CR                             Cancel suffix CR

Add suffix LF                              Cancel suffix LF